## Slide 1
Proposed Mantech Architecture for IFB-CO-11713-CSC May 2006
Existing NATO Digital WAN and PBX System
Proposed Cisco VOIP System
Siemens HiCom 350s
Siemens HiPsath 4000s
Cisco MCS7845-H1 CallManager Appliance w/ v5.X
Cisco 3645 Voice Gateway w/ qty 1 NM-HDV-2E1-60, Dual port 60 channel
E1 PRI
E1 PRI
Dual 10/100 Full Duplex

## Slide 2
Advantages
Uses existing digital WAN infrastructure
allows up to 360 voice ports to be gatewayed from Cisco Ethernet VOIP into the legacy Siemens PBXs in NATO
allows legacy based digital phones to call themselves or new Cisco IP phones, and visa versa
the Cisco MCS7845-H1s can support 7500 IP phones by itself, or can be clustered later with other 7845s for a total of 30000 IP phones. This product has all the hardware and includes CallManager 5.x ( all you need in a CallManager)
if NATO wants to go all IP phones in the future by phasing out the current PBXs and digital lines and going to Dense Wavelength Division Multiplexing, inter-site, it CAN do that at that time continuing to use the Cisco MCS7845-H1 CallManager Appliance

## Slide 3
Solution A (users less than 1km from existing PBXs)
existing PBX
BRI
Cisco 836 Secure Broadband Router
e0
Secure Analog Phone of Customer’s Choice (Perhaps an L3 Comm STE)
Cisco 7912 Basic
Office IP Phone
(supports MLPP)
Existing POTS line

## Slide 4
Solution B (Up to 8km from existing PBXs)
existing PBX
BRI
Cisco 836 Secure Broadband Router
e1
Secure Analog Phone of Customer’s Choice (Perhaps an L3 Comm STE)
Cisco 7912 Basic
Office IP Phone
(supports MLPP)
(Up to 2 IP phones per BRI)
Existing POTS line
e0
Cisco 7912 Basic
Office IP Phone
(supports MLPP)

## Slide 5
Solutions C, D, E (Small remote Site)
existing PBX
RAD E1 CSU/DSU,
model FCD-E1M
Cisco 1841 Integrated Services Router w/ qty 1(max 2) HWIC-4ESW (per 4 IP phones), & qty 1 WIC-2T
e1
Secure Analog Phone of Customer’s Choice (Perhaps an L3 Comm STE)
Cisco 7912 Basic
Office IP Phone
(supports MLPP)
(Up to 8 IP phones per site)
Existing POTS line
e0
Cisco 7912 Basic
Office IP Phone
(supports MLPP)
s0
Fractional Leased Line (Solution C) , OR
Qty 1 Cisco serial cable prod # CAB-530MT=, p/n 72-0797-01
Full E1 (Solution D) ,OR
Full T1 (Solution E)